## Slide 1: HALE Aeroecodesign
S2 Project Report – 26/06/2020
Víctor Manuel GUADAÑO MARTÍN
Tutors: J. Morlier & E. Duriez
Master of Aerospace Engineering - Research Project

## Slide 2: OUTLINE
STATE OF THE ART
GOAL OF THE PROJECT
MILESTONES OF THE PROJECT
RESULTS
CONCLUSIONS
FUTURE WORK
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN

## Slide 3: STATE OF THE ART
HALE ➤ High-Altitude Long Endurance Drone
  Atmospheric satellites or atmosats
  Services conventionally provided by space satellites
  Environment-friendly ➤ Powered by solar energy
  CO2 emissions ➤ Manufacturing and materials
MDO ➤ Multidisciplinary Design Optimization
  Optimum for the interaction of disciplines
  OpenAeroStruct (based on OpenMDAO) ➤ Aerostructural optimization
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
Fig. 1: Airbus-built HALE Zephyr

## Slide 4: GOAL OF THE PROJECT
Refine a modified version of OpenAeroStruct presented in [1]
CO2 footprint optimization of a HALE
Compromise solution between:
  Convergence of the optimization ➤ Efficiency
  Complexity of the model ➤ Realistic
Validation with Facebook’s single-boom HALE [2]
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
Fig. 2: Optimal HALE wing structure [1]
Fig. 3: Facebook’s single-boom HALE [2]
E. Duriez and J. Morlier, “Hale multidisciplinary design optimization with a focus on eco-material selection,” ISAE Supaero, 2020.
D. Colas, N. H. Roberts, and V. S. Suryakumar, “Hale multidisciplinary design optimization Part I: Solar-powered single and multiple-boom aircraft,” in 2018 AviationTechnology, Integration, and Operations Conference, p. 3028, 2018.
[1]
[2]

## Slide 5: MILESTONES OF THE PROJECT
Buckling model
1-cos gust
Different materials
Limit wing surface
Engines
Material components
Buckling model
1-cos gust
Different materials
Limit wing surface
Engines
Material components
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
SEMESTER 3
COMPLETED

## Slide 6: Add a constraint on the wing surface
Reduce snowball effect ➤ Prevent the optimization from diverging
Maximum wing surface threshold ➤ 200 m2
Divergence
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
HALE
Weight
Propulsion
Weight (batteries & solar panels)
Structural
Weight
➤
➤
➤

## Slide 7: Turn material function into OpenMDAO components
Component ➤ The most efficient way for gradient-based optimization
Replace the existing function by the component
Access to material properties database and interpolate:
  Young’s modulus (E)
  Shear modulus (G)
Get to know the OpenMDAO methodology
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
  Failure strength
  CO2 emissions

## Slide 8: Add engines as point masses
Two symmetrical engines ➤ Two symmetrical point masses
New design variable ➤ Engine spanwise location
Same propulsion density as FB single-boom HALE [2]
where dprop is the propulsion density, Mprop is the propulsion
mass, and Pprop is the power needed for propulsion
Reduce the bending moment on the wing due to lift
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
D. Colas, N. H. Roberts, and V. S. Suryakumar, “Hale multidisciplinary design optimization Part I: Solar-powered single and multiple-boom aircraft,” in 2018 AviationTechnology, Integration, and Operations Conference, p. 3028, 2018.
[2]
Fig. 4: Bending moment distribution along semi-span
Engine location

## Slide 9: RESULTS
Variable | Units | HALE of [1] | FB HALE [2] | Results w/o engines | Results w/ engines
Span | m | 97.5 | - | 93.5 | 70.2
Root chord | m | 1.4 | - | 1.4 | 1.4
Taper ratio | - | 0.32 | - | 0.33 | 0.30
Total mass | kg | 378 | 320 | 435 | 362
Wing surface | m2 | 86.6 | 71.8 | 83.4 | 61.3
Aspect ratio | - | 94 | 29 | 105 | 80
CLcruise | - | 1.31 | 1.33 | 1.56 | 1.77
(CL3/2/CD)cruise | - | 44.1 | 40.1 | 57.8 | 72.1
yengine/(b/2) | - | 0 | 0.46 | 0 | 0.79
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
E. Duriez and J. Morlier, “Hale multidisciplinary design optimization with a focus on eco-material selection,” ISAE Supaero, 2020.
D. Colas, N. H. Roberts, and V. S. Suryakumar, “Hale multidisciplinary design optimization Part I: Solar-powered single and multiple-boom aircraft,” in 2018 AviationTechnology, Integration, and Operations Conference, p. 3028, 2018.
[1]
[2]
Table 1: Final design variable values for validation case

## Slide 10: RESULTS
Performance | Units | HALE of [1] | Results w/o engines | Results w/ engines
Cases | - | 24 | 24 | 24
Convergences | - | 7 | 12 | 11
Time | h | 2 | 3 | 4
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
E. Duriez and J. Morlier, “Hale multidisciplinary design optimization with a focus on eco-material selection,” ISAE Supaero, 2020.
[1]
Table 2: Performance values of the optimization for validation case

## Slide 11: CONCLUSIONS
Without engines ➤ Better convergence and same results as in [1]
With engines ➤ Worse convergence than without engines but better results
Same differences with respect to [2] as in [1] ➤ Very high aspect ratio
Need for 1-cosine gust and more complex buckling model
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
E. Duriez and J. Morlier, “Hale multidisciplinary design optimization with a focus on eco-material selection,” ISAE Supaero, 2020.
D. Colas, N. H. Roberts, and V. S. Suryakumar, “Hale multidisciplinary design optimization Part I: Solar-powered single and multiple-boom aircraft,” in 2018 AviationTechnology, Integration, and Operations Conference, p. 3028, 2018.
[1]
[2]

## Slide 12: FUTURE WORK
Limit wing surface
Material components
Engines
Different materials
Buckling model
1-cos gust
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
Young’s modulus
Shear modulus
Yield strength
CO2 emissions
Position
Mass
Curved plates
Compression
Shear
Two materials
  Skins
  Spars
COMPLETED
SEMESTER 3

## Slide 13: Set different materials for different parts of the wing
FUTURE WORK
Currently ➤ Single material for the whole wing
Allow the optimization to use two different materials:
  One for the spars
  One for the skins
Better solution in terms of CO2 footprint
More design variables ➤ Longer optimization
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN

## Slide 14: Introduce a more complex buckling model
FUTURE WORK
Currently ➤ Skins as rectangular flat plates under axial compression
Consider curved plates
Under combined axial compression and shear
Parabolic interaction:
where Rs and RC are the stress ratios for shear and compression
Use of empirical data [3]
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
G. Gerard and H. Becker, “Handbook of structural stability. part 3. buckling of curved plates and shells.,” tech. rep., NATIONAL AERONAUTICS AND SPACE ADMIN-ISTRATION WASHINGTON DC, 1957.
[3]
Fig. 5: Comparison of test data with parabolic interaction curves for curved plates under combined shear and axial compression [3]

## Slide 15: Model a two dimensional discrete gust
FUTURE WORK
Currently ➤ One-dimmensional shear gust
Implement a 1-cosine gust profile [2]:
where wg is the gust velocity, Ude is the derived equivalent gust velocity, Lspan is the aircraft span, a is a factor and y is the spanwise coordinate
Increase bending moment ➤ Penalize large aspect ratios
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
Y. Yang, Y. Chao, and W. Zhigang, “Aeroelastic dynamic response of elastic aircraft with consideration of two-dimensional discrete gust excitation,” Chinese Journal of Aeronautics, 2019.
[4]
Fig. 6: Spanwise distribution of 1-cosine gusts

## Slide 16: Add a constraint on the wing surface
Reduce snowball effect ➤ Prevent the optimization from diverging
  Maximum wing surface threshold ➤ 200 m2
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
Fix some design variables
Make the problem more computationally efficient
  Fix some optimization variables ➤ tapper ratio, root chord…
  Finally not used to compare the results in a better way

## Slide 17: Thanks for your attention!
ANY QUESTION?
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
“True optimization is the revolutionary contribution of modern research to decision processes”
George Dantzig