## Slide 1: HALE Aeroecodesign
S2 – Progress Report
Víctor Manuel GUADAÑO MARTÍN
Tutors: J. Morlier & E. Duriez
Master of Aerospace Engineering - Research Project

## Slide 2: OUTLINE
STATE OF THE ART
GOAL OF THE PROJECT
MILESTONES OF THE PROJECT
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN

## Slide 3: STATE OF THE ART
HALE ➤ High-Altitude Long Endurance Drone
  Atmospheric satellites or atmosats
  Services conventionally provided by space satellites
  Environment-friendly ➤ Powered by solar energy
  CO2 emissions ➤ Manufacturing and materials
MDO ➤ Multidisciplinary Design Optimization
  Optimum for the interaction of disciplines
  OpenAeroStruct (based on OpenMDAO) ➤ Aerostructural optimization
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
Fig. 1: Airbus-built HALE Zephyr

## Slide 4: STATE OF THE ART
Variable | Units | HALE of [1] | FB HALE [2]
Span | m | 97.5 | -
Root chord | m | 1.4 | -
Taper ratio | - | 0.32 | -
Total mass | kg | 378 | 320
Wing surface | m2 | 86.6 | 71.8
Aspect ratio | - | 94 | 29
CLcruise | - | 1.31 | 1.33
(CL3/2/CD)cruise | - | 44.1 | 40.1
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
E. Duriez and J. Morlier, “Hale multidisciplinary design optimization with a focus on eco-material selection,” ISAE Supaero, 2020.
D. Colas, N. H. Roberts, and V. S. Suryakumar, “Hale multidisciplinary design optimization part i: Solar-powered single and multiple-boom aircraft,” in 2018 AviationTechnology, Integration, and Operations Conference, p. 3028, 2018.
[1]
[2]
Table 1: Design variable values for validation case [1]
Fig. 2: Optimal HALE wing structure [1]
Fig. 3: Facebook’s single-boom HALE [2]

## Slide 5: GOAL OF THE PROJECT
Refine a modified version of OpenAeroStruct presented in [1]
CO2 footprint optimization of a HALE
Compromise solution between:
  Convergence of the optimization ➤ Efficiency
  Complexity of the model ➤ Realistic
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
E. Duriez and J. Morlier, “Hale multidisciplinary design optimization with a focus on eco-material selection,” ISAE Supaero, 2020.
[1]

## Slide 6: MILESTONES OF THE PROJECT
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
Task 1: Add a constraint on the wing surface
Task 2: Fix some design variables
Task 3: Turn material function into OpenMDAO component
Task 4: Set different materials for different parts of the wing
Task 5: Introduce a more complex buckling model
Task 6: Add engines as point masses
Task 7: Model a two dimensional discrete gust

## Slide 7: Task 1: Add a constraint on the wing surface
Reduce snowball effect ➤ Prevent the optimization from diverging
  Maximum wing surface threshold
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
Task 2: Fix some design variables
Make the problem more computationally efficient
  Fix some optimization variables ➤ tapper ratio, root chord…

## Slide 8: Task 3: Turn material function into OpenMDAO component
Currently ➤ Function to use material properties
OpenMDAO ➤ Modular implementation in components
Components ➤ More efficient for gradient-based optimization
Replace the function by a component
Get to know the OpenMDAO methodology
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN

## Slide 9: Task 4: Set different materials for different parts of the wing
Currently ➤ Sigle material for the whole wing
Allow the optimization to use two different materials:
  One for the spars
  One for the skins
Better solution in terms of CO2 footprint and weight
More design variables ➤ Longer optimization
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN

## Slide 10: Task 5: Introduce a more complex buckling model
Currently ➤ Skins as rectangular flat plates under axial compression
Consider curved plates
Under combined axial compression and shear
Parabolic interaction:
where Rs and RC are the stress ratios for shear and compression
Use of empirical data [3]
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
G. Gerard and H. Becker, “Handbook of structural stability. part 3. buckling of curved plates and shells.,” tech. rep., NATIONAL AERONAUTICS AND SPACE ADMIN-ISTRATION WASHINGTON DC, 1957.
[3]
Fig. 4: Comparison of test data with parabolic interaction curves for curved plates under combined shear and axial compression [3]

## Slide 11: Task 6: Add engines as point masses
Currently ➤ Propulsion mass in the plane of symmetry
Already implemented in OpenAeroStruct
Two symmetrical engines ➤ Two symmetrical point masses
New design variable ➤ Distance from the plane of symmetry
Reduce the bending moment on the wing due to lift
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN

## Slide 12: Task 7: Model a two dimensional discrete gust
Currently ➤ One-dimmensional shear gust
Implement a 1-cosine gust profile [4]:
where wg is the gust velocity, Ude is the derived equivalent gust velocity, Lspan is the aircraft span, a is a factor and y is the spanwise coordinate
Increase bending moment ➤ Penalize large aspect ratios
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN
Y. Yang, Y. Chao, and W. Zhigang, “Aeroelastic dynamic response of elastic aircraft with consideration of two-dimensional discrete gust excitation,” Chinese Journal of Aeronautics, 2019.
[4]
Fig. 5: Spanwise distribution of 1-cosine gusts

## Slide 13: THANks for your attention!
ANY QUESTION?
Víctor M. GUADAÑO MARTÍN
HALE AEROECODESIGN